## Slide 1: Module 5
Advanced Features: Publication

## Slide 2: Overview

## Slide 3: Overview
Allows central management of configuration.
One project, edited on the publication server (typically the logging or maintenance server), published to remote Workstations for production.

## Slide 4: Publication Server

## Slide 5: Publication Server
The server which publishes the new project version to Workstations
Configured in General Project Settings
Notes: Insert screenshot here

## Slide 6: IPFusion Publication Service

## Slide 7: IPFusion – Project Publication
Windows service installed with IPFusion
Required for publishing
Communicates if the Workstation is available for publication

## Slide 8: Publication Window

## Slide 9: Publication Window

## Slide 10: Publication Window — Workstation Block
Name of the Workstation
Sync Service States
  Green — Service is waiting
  Yellow — Update in Progress
  Red — Service not found
IP Address of the Workstation
Last Published Time
  The color of the date shows the current status of the files
    Red — The last time the files were published to
    White — Published a new update at this time

## Slide 11: Publication Window — Publication Buttons
Publish
  Publish the project files to the selected Workstation.
  When the Workstation receives the update, it will prompt the operator to accept the change.
Force Publish
  When the Workstation receives the update, Runtime will automatically update the project files regardless of user input.

## Slide 12: Publish a Project

## Slide 13: Publish a Project
Click Publish Project in Designer
Select the Workstations to include in the publication request
  Press Ctrl + A to include all Workstations
Select Publish or Force Publish
If the Publication Service is running on the Workstation, its files will be updated accordingly
When started, Runtime will automatically load the most recently published project received

## Slide 14: Example

## Slide 15: Module 5 Complete